## Slide 1
Gembar + Gembox 更新
Charlie Becquet
Device Group
3 February 2025

## Slide 2
Test Results and Analysis
Gembar User Test Update Gembar Big Vacuum High Temperature Test Gembar Intense Test Gembar High Temp High Humidity Test Gembar Long Puff Test Gembox User Test Update Necessary Design Changes for Gembox
Gembox Big Vacuum High Temperature Test Gembox Intense Test Gembox Viscosity Compatibility Test Gembox High Temp High Humidity Test Gembox Long Puff Test Sensory Comparison of Pine Stick New Product and Oil Coil Gembar + Gembox Pine Stick Test Update

## Slide 3
Gembar User Test Update
Sample | Username | Transaction Date | Media Filled? | Filling Volume | Resistance Before Use | Distribution Date | Progress | Return Date | Resistance After Collection | Voltage | Power | Issue? | Comments?
1-13 Batch User-1 | Charlie | 1/2/2025 | 1.1 mcp D9 | 2mL | 2.3 | 1/13/2025 | 75% | 1/24/2025 | 2.3 | 3.2 | 4.45217391 | Lost equipment yesterday under the lab workbench. No issues before that. | Good performance
1-13 Batch User-2 | Leon | 1/2/2025 | 1.1 mcp D9 | 2mL | 2.3 | 1/13/2025 | 90% | 1/23/2025 | 2.3 | 3.2 | 4.45217391 | No issue | Good performance
1-13 Batch User-3 | Nellie | 1/2/2025 | 1.1 mcp D9 | 2mL | 2.3 | 1/13/2025 | 60% | 1/22/2025 | 2.3 | 3.2 | 4.45217391 | Stopped activating at 60% remaining | Failure seems to be due to poor pin connection. Heater is undamaged, resistance is nominal.
1-13 Batch User-4 | Jordan | 1/2/2025 | 1.1 mcp D9 | 2mL | 2.3 | 1/13/2025 | 50% |  |  | 3.2 | 4.45217391 | No issues so far | 
1-22 Batch User-5 ROSIN | Charlie | 1/29/2025 | MPX Rosin | 2mL | 2.3 | 1/29/2025 | 60% |  |  | 3.2 | 4.45217391 | Slight discoloration | 
2-3 Batch User-1 | Charlie | 2/4/2025 | 663kcp D9 | 2mL | 2.3 | 2/5/2025 | 0% |  |  | 3.2 | 4.45 |  | 
2-3 Batch User-2 | Isabel | 2/4/2025 | 663kcp D9 | 2mL | 2.3 | 2/5/2025 | 0% |  |  | 3.2 | 4.45 |  | 
2-3 Batch User-3 | Leland | 2/4/2025 | 663kcp D9 | 2mL | 2.3 | 2/5/2025 | 0% |  |  | 3.2 | 4.45 |  | 
1-13 Batch User-2
1-13 Batch User-3
1-22 Batch User-5 Rosin
Gembar user testing is promising. Only one failure to date, and it seems to be a pin connection issue. Compared to Gembox, the discoloration of shellac seems less obvious. Leakage was very small in user testing. Today we filled and distributed 3 extra new batches of samples.

## Slide 4
Gembar 1-22 Large Peak Empty Height T Test Results
Design and Oil | Power | Resistance | Power | TPM (mg/puff) and Standard Deviation | Suction Pressure (kPa) | SDR Results | Notes
Gembar BHHT-1 800kcp D8 | 4.45W | 2.3 | 60mL/3s/30s | 2.63, 0.49 | 0.464 | Pass | No clogging
Gembar BHHT-2 800kcp D8 | 4.45W | 2.3 | 60mL/3s/30s | 3.07, 0.27 | 0.379 | Tentative Pass | No clogging, low draw force
Gembar BHHT-3 800kcp D8 | 4.45W | 2.3 | 60mL/3s/30s | 2.2, 0.83 | 0.296 | Tentative Pass | No clogging, low draw force
Gembar BHHT-4 800kcp D8 | 4.45W | 2.3 | 60mL/3s/30s | 2.36, 0.1 | 0.692 | Pass | No clogging
Gembar BHHT-5 800kcp D8 | 4.45W | 2.3 | 60mL/3s/30s | 0,0 | 0.382 | Fail | No clogging, no activation

## Slide 5
Gembar 1-22 Intense 测试结果
Design and Oil | Power | Resistance | Regime | TPM (mg/puff) and Standard Deviation | Usage Efficiency (%) | SDR Result | Notes
Gembar Intense-1 800kcp D8 | 4.45W | 2.3 | 200mL/3s/30s | 3.38, 0.91 | 79.0% | Pass | Sample is completely empty – 79% efficiency usage
Gembar Intense-2 800kcp D8 | 4.45W | 2.3 | 200mL/3s/30s | 3.79, 0.49 | N/A | Ongoing | 
Gembar Intense-3 800kcp D8 | 4.45W | 2.3 | 200mL/3s/30s | 3.76, 0.98 | N/A | Ongoing | 
Gembar Intense-4 800kcp D8 | 4.45W | 2.3 | 200mL/3s/30s | 4.06, 0.99 | N/A | Ongoing | 
Gembar Intense-5 800kcp D8 | 4.45W | 2.3 | 200mL/3s/30s | 3.3, 0.28 | N/A | Ongoing | 
Successfully prevented inlet wall clogging

## Slide 6
Gembar 1-22 High Temperature and High Humidity Results
HTHH-1: Upright direction, air intake not blocked
HTHH-2: Inverted direction, air intake blocked
This is a very minor failure - please carefully look for solutions that may prevent further blockage. I recommend using dual air intakes, similar to what the CPS2910 team did.

## Slide 7
Gembar 1-22 Long Puff 测试结果
Design and Oil | Power | Resistance | Regime | Pulling resistance (kPa) | SDR Result | Notes
Gembar Long-1 700kcp D8 | 4.45W | 2.3 | 100mL/5s, 160mL/8s, 200mL/10s | 0.696 | Pass | No problems
Gembar Long-2 700kcp D8 | 4.45W | 2.3 |  | 0.365 | Tentative Pass | Low traction and low TPM. No burns or any other problems.
Gembar Long-3 700kcp D8 | 4.45W | 2.3 |  | 0.798 | Pass | No problem
Gembar Long-4 700kcp D8 | 4.45W | 2.3 |  | 0.586 | Tentative Pass | Low TPM, longer suction time, but no burning
5s Puff
8s Puff
10 second puff

## Slide 8
Gembox User Testing Update
Insufficient user testing for D9 - The focus has always been on Gembar and the 510 model. Significant modifications are needed for the angle of the air inlet and the gasket above the air inlet. During the sulfur candle user test, batches 12-11 with a wall around the inlet performed best. However, there is not enough D9 data to support this.
Sample | Username | Transaction Date | Filled Media | Fill Volume | Resistance Before Use | Issuance Date | Progress | Return Date | Resistance After Collection | Voltage | Power | Issues? | Comments?
1-13 Batch Rosin-1 | Charlie | 1/15/2025 | MPX Rosin | 2 | 2.3 | 1/15/2025 | 30% | 1/21/2025 | 2.3 | 3.2 | 4.45 | Clog | Sample quickly clogged at the inlet.
1-13 Batch Rosin-2 | Leland | 1/15/2025 | MPX Rosin | 2 | 2.3 | 1/15/2025 | 50% |  | 2.3 | 3.2 | 4.45 |  | Leland's sample did not clog.
1-13 Batch D9-1 | Charlie | 1/15/2025 | 800kcp D9 | 2 | 2.3 | 1/15/2025 | 40% | 2/3/2025 | 2.3 | 3.2 | 4.45 | Clog | Inlet clogged
1-13 Batch D9-2 | Leon | 1/15/2025 | 800kcp D9 | 2 | 2.3 | 1/15/2025 | 50% | 1/22/2025 | 2.3 | 3.2 | 4.45 | Clog | Inlet clogged
12-11 Batch Rosin-1 | Charlie | 1/17/2025 | MPX Rosin | 2 | 2.3 | 1/17/2025 | 80% | 1/29/2025 | 2.3 | 3.2 | 4.45 | Clog | Clogs at the inlet after using 80%. Severe discoloration.
12-11 Batch Rosin-2 (1mL) | Jim | 1/22/2025 | MPX Rosin | 1 | 2.3 | 1/22/2025 | 20% |  | 2.3 | 3.2 | 4.45 |  | No updates available
1-13 Batch D9-2 – 剩余 50% 时堵塞
Vapor Pathway – Expecting oil here
Wrong direction – We should not see oil here

## Slide 9
Necessary Design Changes for Gembox
Observe these three figures. The first figure shows unnecessary condensation directly above the inlet. This increases the risk of clogging and further reduces overall efficiency. Figure two prevents unnecessary steam reflection and condensation above the inlet. This simple modification is necessary to prevent inlet clogging. Figure three reintroduces an inlet wall that existed in the batch from December 11, 2024. This will reduce oil leakage into the inlet space by 75%. User testing with incense has shown that this reduces clogging.
Figure 1: Current Gembox Vapor Pathway (Front cross-section - pins removed)
Figure 2: Improved Gembox Vapor Passage (Front cross-section - pins removed)
1-13 Batch D9-2 – Clogged at 50% remaining
Vapor Pathway – Oil expected here
Wrong direction – We should not see oil here
Figure 3: Improved Gembox Vapor Passage + Inlet Wall (Front cross-section - pin removed)
The inlet wall is transparent for easy viewing.
When making design changes: Ensure adherence to proper Design of Experiments (DoE) procedures. This means that all modifications should be isolated and tested before introducing the final design.
The inlet wall has two purposes: to prevent oil entry, and to guide air directly to the heater.

## Slide 10
Gembox 1-22 Big Headspace High T 测试结果
Design and Oil | Power | Resistance | Regime | TPM (mg/puff) and Standard Deviation | Draw Pressure (kPa) | SDR Result
Gembox BHHT-1 800kcp D8 | 4.45W | 2.3 | 60mL/3s/30s | 2.65, 0.19 | 0.498 | Pass
Gembox BHHT-2 800kcp D8 | 4.45W | 2.3 | 60mL/3s/30s | 2.29, 0.24 | 0.531 | Pass
Gembox BHHT-3 800kcp D8 | 4.45W | 2.3 | 60mL/3s/30s | 2.49, 0.12 | 0.608 | Pass
Gembox BHHT-4 800kcp D8 | 4.45W | 2.3 | 60mL/3s/30s | 1.73, 0.24 | 0.802 | Pass
Gembox BHHT-5 800kcp D8 | 4.45W | 2.3 | 60mL/3s/30s | 1.98, 0.17 | 0.628 | Pass
Due to the slope here, oil accumulates above the inlet - remove it!

## Slide 11
Gembox 1-22 Intense 测试结果
Design and Oil | Power | Resistance | Regime | TPM (mg/puff) and Standard Deviation | SDR Result | Notes
Gembox Intense-1 800kcp D8 | 4.45W | 2.3 | 200mL/3s/30s | 2.5, 0.69 | Ongoing | Testing is still in progress. Efficiency will be reported next week.
Gembox Intense-2 800kcp D8 | 4.45W | 2.3 | 200mL/3s/30s | 3.05, 0.96 | Ongoing | 
Gembox Intense-3 800kcp D8 | 4.45W | 2.3 | 200mL/3s/30s | 2.98, 0.88 | Ongoing | 
Gembox Intense-4 800kcp D8 | 4.45W | 2.3 | 200mL/3s/30s | 3.37, 0.93 | Ongoing | 
Gembox Intense-5 800kcp D8 | 4.45W | 2.3 | 200mL/3s/30s | 2.94, 0.96 | Ongoing | 
So far, performance looks good. The initial low TPM was due to the impactor issue.

## Slide 12
Gembox 1-22 Viscosity Compatibility Test Results
Design and Oil | Power (voltage set to 3.2V) | Resistance | Regime | TPM (mg/puff) and Standard Deviation | SDR Result | Notes
Gembox 43kcp D8 | 4.45W | 2.3 | 60mL/3s/30s | 2.9, 0.38 | Pass | 
Gembox 136kcp D8 | 4.45W | 2.3 | 60mL/3s/30s | 2.49, 0.5 | Pass | 
Gembox 1.2mcp D8 | 4.45W | 2.3 | 60mL/3s/30s | 2.17, 0.26 | Pass | 
Gembox 4mcp D8 | 4.45W | 2.3 | 60mL/3s/30s | 1.12, 0.6 | Tentative Pass | Low TPM is mainly due to thicker bubbles. When adequately humidified, the TPM is ~2 mg/spray.
Gembox (From QS-1, 3.4V) 800kcp D8 | 5W (3.4V*) | 2.3 | 60mL/3s/30s | 3.39, 0.4 | Pass | 
The TPM of 4mcp oil decreased because thick bubbles on the heater obstructed capillary action.
The heater for the 43kcp D8 sample seems to be cracked. Oil was observed above the air inlet, which can ultimately cause clogging. The side walls of the air inlet should minimize this issue. Leakage behind the heater indicates a risk of further clogging. We should study increasing the distance between the air inlet and the heater.

## Slide 13
Gembox 1-22 Long Puff 测试结果
Design and Oil | Power | Resistance | Regime | Draw Resistance | SDR Result | Notes
Gembox Long-1 700kcp D8 | 4.45W | 2.3 | 100mL/5s, 160mL/8s, 200mL/10s | 0.842 | No problem | 
Gembox Long-2 700kcp D8 | 4.45W | 2.3 |  | 0.528 | No problem | 
Gembox Long-3 700kcp D8 | 4.45W | 2.3 |  | 1.032 | No problem | 
Gembox Long-4 700kcp D8 | 4.45W | 2.3 |  | 0.392 | Draw Resistance 很低 | No activation issues even at low tensile strength
5s Puff
8s Blow
10s 吹

## Slide 14
Gembox 1-22 High Temperature and Humidity Results
Leakage only behind the steam path. This indicates the slope on the silicon diaphragm
HTHH-6

## Slide 15
Sensory comparison of new and old coils for musk sticks
User | 1 | 2 | 3 | 4
Nellie | New Coil 2 | New-Working-1 | Old Coil 1 | Old-Working-2
Leland | Old Coil 1 | New-Working-1 | New Coil 2 | Old-Working-2
Charlie | Old Coil 1 | New-Working-1 | New Coil 2 | Old-Working-2
Ranking (1 is best)
Based on 3 rapid sensory tests, there does not appear to be any significant difference between the new and old coils. Old-working-2 is consistently the worst, while new-working-1 is consistently second best.
Objective: To identify any differences between the new and old coils. The test passes if the new coil is better than or equal to the old one.

## Slide 16
Gembar + Gembox Pine Freshener Test Update
Gembar: Currently undergoing a 2mL pine freshener user test, with usage at 50%. Discoloration has been observed, but there is no noticeable change in scent. No blockages or oil leaks have occurred so far. Gembox: Blockage found in the 2mL pine freshener user test samples. The batch from December 11, 2024 (black casing) first blocked when approximately 20% of the oil remained. The batch from 1-22-2025 (transparent casing) began blocking at 50% remaining and experienced severe clogging at 40% remaining. This further illustrates the advantage of the old air inlet. Discoloration is very obvious as the oil level drops.

## Slide 17
Thank you